| Bodman Park  Middletown Township (N.J.)  ADA Transition Plan 50 Market St. (Fairview) Spring 2008 |
| --- |
| S |  |  |  |  |  |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Miscellaneous Parking | The lot that serves the shelter and restrooms has no designated parking. The route from this parking lot to the sidewalk, crosses a 3” threshold( | Minimum 1 “van accessible” space and 1 standard accessible space. Access aisles serving van spaces shall be at least 96” wide and aisles serving standard accessible spaces shall be at least 60” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Two spaces may share a common access aisle. Actual numbers of total accessible spaces needed should be determined by the total estimated number of spaces in this lot per table under 4.1.2 (4.1.2(5)(b) & 4.6). Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). | H H | $500 $500 |  |
| Public Restrooms | The route to the restrooms is rough and uneven grass( Men’s/Women’s: Signage is located on doors. The sink has 28” knee clearance to apron, an exposed drain pipe and the push faucet control requires 8 lbs. force to operate. There is no rear grab bar in accessible toilet stalls and toilets are 15 ½” high. The urinal in the men’s room is 26” high to rim. The toilet stall lock in the men’s room requires pinching and turning of the wrist to operate. The flush control in the women’s accessible toilet stall is located on far side of toilet. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign (4.30.6). Lavatories shall provide a clearance of at least 29” above the finish floor to the bottom of the apron. Hot water and drain pipes exposed under sinks shall be insulated or otherwise configured so as to protect against contact. The force required to activate controls shall be no greater than 5 lbs. (4.19 & 4.27.4). A grab bar at least 36” long shall be located behind the water closet, with one end no farther than 6” from the inside corner of the stall. The height of water closets shall be 17” to 19”, measured to the top of the toilet seat (Figure 30 & 4.16.3). Urinals shall be stall-type or wall-hung with an elongated rim at a maximum of 17” above the finish floor. Flush controls shall be mounted no more than 44” above the finish floor (4.18). Handles, pulls, latches, locks, and other operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate (4.13.9). Flush controls shall be mounted on the wide side of toilet areas (4.16.5). | H H M M+ L L+ L+ | $3,500 $0 $500 $750 $1,500 $40 $200 |  |
| Covered Shelter (Pavilion) | The route to the shelter is rough and uneven grass. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). Recommendation: install accessible picnic tables and barbecue grills that are connected to the shelter. | H | $2,800 |  |
| Play Area | The route to the playground consists of rough and uneven grass. A threshold up to 5” encompasses the play equipment. The play equipment surface is engineered wood chips. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). Recommendation: this material has been generally accepted as “ADA compliant”, however, to maintain an adequate firm and level surface free of thresholds, this surface must be constantly maintained. We recommend using a rubber or corked surface. There are no ADA enforceable standards for playground areas, only guidelines at the present time; however, program access must still be met. | M- L+ L+ | $2,500 $500 $3,000 |  |
| MYAA Ball Fields | There are no designated parking spaces (grass/dirt) and the route to the bleacher seating area’s consists of rough and uneven grass/dirt. There are no wheelchair seating locations at bleacher seating. Concessions counter is 45 ½” high. | Recommendations: disperse at least 3 accessible spaces to serve the ball fields, one of which should be “van accessible”. Provide a connecting accessible route from parking to the other ball field amenities (bleachers, concessions, etc.). Recommendation: install at least one location as wheelchair accessible seating at each bleacher seating area. Ensure that the location provides an unobstructed line of sight. The designated wheelchair seating area should be large enough for at least 1 wheelchair user and 1 companion. A 60” by 60” minimum area would be preferred. Designation could be accomplished by painting the universal symbol of access on the pavement. Counters maximum height shall be 36” and minimum length shall be 36” (7.2). | H M M | $9,000 $1,000 $500 |  |
| Basketball Courts | No accessible parking spaces exist. The route to the courts consists of rough and uneven grass. | At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Two accessible spaces may share a common access aisle (4.1.2(5)(b) & 4.6). At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | M+ M- | $500 $2,500 |  |
| Maintenance Building Carpenter Shop Mechanics Shop Supervisors Office |  | Recommendation/Note: these structures have no public access and are used by Township staff only. We are not recommending any immediate barrier removal actions. If in the event that the future usage changes, barrier removal should be addressed for basic access. | -- | -- |  |

This excessive threshold exists at the parking lot that			The route to the restrooms is rough and uneven grass.

serves the restroom facility.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $5,240 |
| Medium’s | $8,250 |
| High’s | $11,800 |
| TOTAL | $25,290.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.