| Camp Hope  Middletown Township (N.J.)  ADA Transition Plan Orchard Hill Rd. (Lincroft) Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | There are no designated accessible parking spaces. | Minimum 1 “van accessible” space and 1 standard accessible space. Access aisles serving van spaces shall be at least 96” wide and aisles serving standard accessible spaces shall be at least 60” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Two spaces may share a common access aisle. Parking spaces and access aisles shall be level with surface slopes not exceeding 1:50 (2%) in all directions (4.1.2(5)(b) & 4.6). | H | $1,000 |  |
| Pedestrian Paths of Travel | The route to the restrooms crosses rough and uneven grass. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | M+ | $2,000 |  |
| Swimming Pool | The pool does not offer access to the water. | Recommendation: install an independently operated device such as a lift pump to serve at least one pool. | M | $5,000 |  |
| Public Restrooms | Men’s/Women’s: No signage exists. Sinks have 28” knee clearance to apron and exposed drain pipes. The toilet in accessible stalls are 15 ½” high. No grab bar exists behind toilets and door locks require turning of the wrist to operate. The toilet flush control in the women’s stall is located on the far side of the toilet. The urinal in the men’s room is 24” high to rim. The paper towel dispenser in the men’s room is 56” high (forward reach). | Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille (4.30.4 & 4.30.6). Lavatories shall provide a clearance of at least 29” above the finish floor to the bottom of the apron. Hot water and drain pipes exposed under sinks shall be insulated or otherwise configured so as to protect against contact (4.19) The height of water closets shall be 17” to 19” measured to the top of the toilet seat The rear grab bar shall be at least 36” long. All grab bars shall be located 33” to 36” above the finish floor to the top gripping surface. Handles, pulls, latches, locks, and other operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate (4.16 & 4.13.9). Flush controls shall be mounted on the wide side of toilet areas (4.16.5). Urinals shall be stall-type or wall-hung with an elongated rim at a maximum of 17” above the finish floor. Flush controls shall be mounted no more than 44” above the finish floor (4.18.2 & 4.18.4). 48” maximum forward reach (4.2.5). | M M M L+ L L+ | $100 $300 $500 $300 $1,500 $100 |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $1,900 |
| Medium’s | $7,900 |
| High’s | $1,000 |
| TOTAL | $10,800.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.