| Church Street Park  Middletown Township (N.J.)  ADA Transition Plan Church Street (Near Leonardville Rd.) Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Accessible Paths of Travel | The route to access the park from street level crosses a curb. The playground is not on an accessible route (rough and uneven grass). | Curb ramps complying with 4.7 shall be provided wherever an accessible route crosses a curb (4.7.1). At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | M+ L+ | $500 $2,500 |  |
| Play Ground | A threshold up to 5” encompasses the play equipment. The play equipment surface is engineered wood chips. | Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). Recommendation: this material has been generally accepted as “ADA compliant”, however, to maintain an adequate firm and level surface free of thresholds, this surface must be constantly maintained. We recommend using a rubber or corked surface. There are no ADA enforceable standards for playground areas, only guidelines at the present time; however, program access must still be met. | L+ L+ | $500 $3,000 |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $5,000 |
| Medium’s | $500 |
| High’s | $0 |
| TOTAL | $5,500.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.