| Croydon Hall Complex  Middletown Township (N.J.)  ADA Transition Plan 900 Leonardville Road Spring 2008 |
| --- |
| S |  |  |  |  |  |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| PARKS & REC. ADMIN. SCHOOL BLD. |
| Miscellaneous Parking | One signed accessible space exists but does not indicate “van accessible”. The slope of the ground is 3%. The parking space partially obstructs the curb ramp( | An additional sign "Van-Accessible" shall mounted below the symbol of accessibility on at least 1 space per 4.1.2(5)(b). Parking spaces and access aisles shall be level with surface slopes not exceeding 1:50 (2%) in all directions (4.6). Recommendation: switch the location of the existing accessible space and access aisle so that the access aisle is nearest to the curb ramp. | L+ M+ | $3,000 $500 |  |
| Pedestrian Paths of Travel | The route from the accessible parking to the facility entrance crosses an area with a 15% slope (sides of another curb ramp)( | If a curb ramp is located where pedestrians must walk across the ramp, it shall have flared sides; the maximum slope of the flare shall be 1:10 or 10% (4.7.5). | H | $600 |  |
| Entrance | The south entrance is 30” wide. | Doorways shall have a minimum clear opening of 32” with the door open 90 degrees, measured between the face of the door and the opposite stop (4.13.5). | H | $750 |  |
| Interior Features | Interior rooms and spaces (exits, offices, classrooms, etc.) have signage in inaccessible locations and formats. Office entrances are 28” wide. Classroom entrances are 30” wide. Classrooms lack alarm notification devices. Parks & Rec. Office: Entrance door has a panel type handle( The transaction counter is more than 44” high. Men’s/Women’s: Signage is not in an accessible format or location. Entrance doors require 15 lbs. force to open. Sink faucets require 10 lbs. force to operate. Toilet flush controls in accessible stalls are located on far side of toilets. Toilet paper dispensers are more than 40” from rear walls( | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door (4.30.4 & 4.30.6). Doorways shall have a minimum clear opening of 32” with the door open 90 degrees, measured between the face of the door and the opposite stop (4.13.5). Recommendation: it would be acceptable to modify at least one class room and one office entrance incase a service/program needs to be relocated to the accessible room. At a minimum, visual signal appliances shall be provided in buildings and facilities in each of the following areas: restrooms and any other general usage areas (e.g., meeting rooms), hallways, lobbies, and any other area for common use (4.28.1). Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs (4.13.9). Counters maximum height shall be 36” and minimum length shall be 36” (7.2). Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door (4.30.4 & 4.30.6). 5 lbs. maximum for interior hinged doors (4.13.11). Controls and operating mechanisms shall be operable with one hand and shall not require tight grasping, pinching, or twisting of the wrist. The force required to activate controls shall be no greater than 5 lbs. (4.27.4). Flush controls shall be mounted on the wide side of toilet areas. Toilet paper dispensers shall be below the grab bar and at least 19” above the floor and no farther than 36” from the rear wall, measured to the far side of the dispensers (4.16.5 & Figure 30(d)). | H M+ H H M H M L+ M- | $500 $7,000* $1,500 $150 $250 $100 $0 $50 $500 |  |
|  |  | HISTORICAL BLD. (WHITE HOUSE) |  |  |  |
| Exterior Pedestrian Paths of Travel | the entrance ramp has a handrail on one side only and has inadequate height, edge protection and extensions( | If a ramp run has a rise greater than 6” or a horizontal projection greater than 72”, then it shall have handrails on both sides. Top of handrail gripping surfaces shall be mounted between 34” and 38” above ramp surfaces. Ramps and landings with drop-offs shall have curbs, walls, railings, or projecting surfaces that prevent people from slipping off the ramp. Curbs shall be a minimum of 2” high. If handrails are not continuous, they shall extend at least 12” beyond the top and bottom of the ramp segment and shall be parallel with the floor or ground surface (4.8.5). | H | $2,500 |  |
| Entrance | The north entrance has hardware that requires pinching of the hand to operate( The entrance has a 1 ½” threshold and is 26” wide( | Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs (4.13.9). Thresholds at doorways shall not exceed ½” beveled. Doorways shall have a minimum clear opening of 32” with the door open 90 degrees, measured between the face of the door and the opposite stop (4.13). Recommendation: if such a modification is deemed to disturb the historical integrity of the structure, the program should be relocated to an accessible location as necessary. | H H | $100 $1,200 |  |
| Public Restroom | The existing restroom is not accessible due to numerous structural limitations. | Recommendation: if providing an accessible restroom is deemed to disturb the historical integrity of the structure, signage should be installed that gives the location of the nearest accessible restroom within the Complex. | M | ** |  |
|  |  | SENIOR CENTER BLD. |  |  |  |
| Parking | Three spaces are signed as accessible but none have “van accessible” designation or access aisles( Ground surfaces slope up to 6%. | At least one accessible space shall be designated as “van accessible”. Access aisles serving van spaces shall be at least 96” wide and aisles serving standard accessible spaces shall be at least 60” wide. Two spaces may share a common access aisle (4.1.2(5)(b) & 4.6). Parking spaces and access aisles shall be level with surface slopes not exceeding 1:50 (2%) in all directions (4.6.3). | H M | $1,500 $3,500* |  |
| Exterior Pedestrian Paths of Travel | The curb ramp at street level has a 3” threshold( The east sidewalk has a 1” change in levels( | Transitions from ramps to walks, gutters, or streets shall be flush and free of abrupt changes (4.7.2). Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). | H M+ | $500 $200 |  |
| Entrance | Door opening hardware consists of a latch that requires pinching to operate. | Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs (4.13.9). | H | $50 |  |
| Interior Features | Exit signs are not in accessible formats and locations. The bingo hall, pool room and restrooms lack alarm notification devices. The pool room entrance is 28” wide. One lowered drinking fountain in the east wing exists. Men’s/Women’s Restrooms: Doors require 10 lbs. force to open. Signage is mounted on doors. Door opening hardware consists of round knobs. Entrances have 8” maneuvering clearance width on pull sides. Mirrors are 44” high to reflective surfaces. Sink drain pipes are exposed. The soap dispenser in the men’s room is 50” high (forward reach only). Accessible toilet stalls have the following barriers: toilet paper dispensers located above side grab bars, toilets 16” center from adjacent walls. The flush control in the men’s accessible stall is located on far side of toilet. East Wing Men’s/Women’s: Signage is mounted on doors and lacks accessible format. Entrances have 1” thresholds. The maneuvering clearance depth on the pull side of the men’s entrance is 42”. Entrance doors require 7 lbs. force to open. Sink drain pipes are exposed and faucets require 10 lbs. force to operate. Mirrors are 46” high to reflective surfaces. The paper towel dispenser in the women’s room has 28” clear floor space width. The latch side approach to accessible toilet stalls is 38 ½ Accessible toilet stalls have the following barriers: 15 ½” high toilets, 36” long side grab bars, toilet paper dispensers located above side bars and toilet at 20” center from side wall (women’s). | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door (4.30.4 & 4.30.6). At a minimum, visual signal appliances shall be provided in buildings and facilities in each of the following areas: restrooms and any other general usage areas (e.g., meeting rooms), hallways, lobbies, and any other area for common use (4.28.1). Doorways shall have a minimum clear opening of 32” with the door open 90 degrees, measured between the face of the door and the opposite stop (4.13.5). Where only one drinking fountain is provided on a floor there shall be a drinking fountain which is accessible to individuals who use wheelchairs and one accessible to those who have difficulty bending or stooping (4.1.3(10)(a)). 5 lbs. maximum for interior hinged doors (4.13.11). Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign (4.30.6). Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs (4.13.9). Front approaches to pull side of swinging doors shall have maneuvering space that extends from the hinge side of the door to 18” minimum, 24” preferred, beyond the latch side of the door and 60” minimum perpendicular to the doorway (Figure 25(a)). Mirrors shall be mounted with the bottom edge of the reflecting surface no higher than 40” above the finish floor (4.19.6). Hot water and drain pipes exposed under sinks shall be insulated or otherwise configured so as to protect against contact (4.24.6). 48” maximum forward reach (4.2.5). Toilet paper dispensers shall be below the grab bar and at least 19” above the floor and no farther than 36” from the rear wall, measured to the far side of the dispensers. The centerline of the water closet is 18” from the side wall (Figure 30(a) & 30(d)). Flush controls shall be mounted on the wide side of toilet areas (4.16.5). Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door (4.30.4 & 4.30.6). Thresholds at doorways shall not exceed ½” beveled (4.13.8). Front approaches to pull side of swinging doors shall have maneuvering space that extends beyond the latch side of the door 60” minimum perpendicular to the doorway (Figure 25(a)). 5 lbs. maximum for interior hinged doors (4.13.11). Controls and operating mechanisms shall be operable with one hand and shall not require tight grasping, pinching, or twisting of the wrist. The force required to activate controls shall be no greater than 5 lbs. Hot water and drain pipes exposed under sinks shall be insulated or otherwise configured so as to protect against contact (4.27.4 & 4.24.6). Mirrors shall be mounted with the bottom edge of the reflecting surface no higher than 40” above the finish floor (4.19.6). 30” minimum width (4.2.4.1). 42” minimum (Figure 30(a)). The height of water closets shall be 17” to 19”, measured to the top of the toilet seat. Side grab bars shall be at least 40” long. Toilet paper dispensers shall be below the grab bar and at least 19” above the floor and no farther than 36” from the rear wall, measured to the far side of the dispensers. The centerline of the water closet is 18” from the side wall (4.16.3 & Figure 30). | H H L+ L M M+ M+ M L M L+ M- L+ H M M M M L L+ M M | $150 $1,000 $800 $400 $0 $50 $100 $2,000* $100 $100 $50 $4,500 $300 $100 $200 $1,000* $0 $150 $100 $50 $2,000* $4,500 |  |
| Nutrition Center | The exterior entrance has panel type handles. Exit signs are not in accessible formats and locations. Men’s/Women’s Restrooms: Entrances have 1” thresholds. Signage is mounted on doors. Doors require more than 8 lbs. force to open. The maneuvering clearance depth on the pull side of the men’s entrance is 43”( Restrooms lack alarm notification devices. Sink pipes are exposed and faucets require 15 lbs. force to operate. Mirrors are 46” high to reflective surfaces. The latch side approach to accessible toilet stalls is 38 ½”( The accessible toilet stalls have the following barriers: 36” long side grab bars, 15 ½” high toilets and toilet flush control on far side of toilet (men’s only). | Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs (4.13.9). Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door (4.30.4 & 4.30.6). Thresholds at doorways shall not exceed ½” beveled (4.13.8). Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign (4.30.6). 5 lbs. maximum for interior hinged doors (4.13.11). Front approaches to pull side of swinging doors shall have maneuvering space that extends from the hinge side of the door, beyond the latch side of the door and 60” minimum perpendicular to the doorway (Figure 25(a)). At a minimum, visual signal appliances shall be provided in buildings and facilities in each of the following areas: restrooms and any other general usage areas (e.g., meeting rooms), hallways, lobbies, and any other area for common use (4.28.1). Hot water and drain pipes exposed under sinks shall be insulated or otherwise configured so as to protect against contact. Controls and operating mechanisms shall be operable with one hand and shall not require tight grasping, pinching, or twisting of the wrist. The force required to activate controls shall be no greater than 5 lbs. (4.24 & 4.27.4). Mirrors shall be mounted with the bottom edge of the reflecting surface no higher than 40” above the finish floor (4.19.6). 42” minimum (Figure 30(a)). Side grab bars shall be at least 40” long. The height of water closets shall be 17” to 19”, measured to the top of the toilet seat. Flush controls shall be mounted on the wide side of toilet areas (4.16 & Figure 30). | H H M M+ M M H M+ L L+ M | $50 $100 $400 $100 $0 $1,000* $1,000 $150 $100 $2,000* $800* |  |
|  |  | PLAYGROUND |  |  |  |
| Parking | Accessible spaces lack “van accessible” designation. | An additional sign "Van-Accessible" shall mounted below the symbol of accessibility on at least 1 space per 4.1.2(5)(b). | M | $50 |  |
| Play Area | The play equipment surface is engineered wood chips and a 2” threshold exists. | Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). Recommendation: this material has been generally accepted as “ADA compliant”, however, to maintain an adequate firm and level surface free of thresholds, this surface must be constantly maintained. We recommend using a rubber or corked surface. There are no ADA enforceable standards for playground areas, only guidelines at the present time; however, program access must still be met. | L | $3,000 |  |
|  |  | GYMNASIUM BLD. |  |  |  |
| Parking | Two spaces are signed as accessible but none are designated as “van accessible”. The access aisle is 60” wide. | At least one accessible space shall be designated as “van accessible”. Access aisles serving van spaces shall be at least 96” wide and aisles serving standard accessible spaces shall be at least 60” wide. Two spaces may share a common access aisle (4.1.2(5)(b) & 4.6). | M+ | $500 |  |
| Exterior Pedestrian Paths of Travel | The curb ramp that serves the parking area has a 2” lip( | Transitions from ramps to walks, gutters, or streets shall be flush and free of abrupt changes (4.7.2). | H | $500 |  |
| Interior Features | Exit signs are not in accessible formats or locations. Interior hinged doors require more than 8 lbs. force to open. The gym entrance door has 1 panel type handle( There are no designated wheelchair seating areas in the gym. The stairway has a handrail on one side only and it lacks adequate extensions. | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door (4.30.4 & 4.30.6). 5 lbs. maximum for interior hinged doors (4.13.11). Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs (4.13.9). Recommendation: install at least one wheelchair seating location near the end of the bleachers. This space should be large enough to accommodate at least 1 wheelchair user and 1 companion. Designation could be accomplished by painting the universal symbol of access on the ground surface. Seating dimensions should comply with Figure 46. Stairways shall have handrails at both sides of all stairs. If handrails are not continuous, they shall extend at least 12” beyond the top riser and at least 12” plus the width of one tread beyond the bottom riser. At the top, the extension shall be parallel with the floor or ground surface. At the bottom, the handrail shall continue to slope for a distance of the width of one tread from the bottom riser; the remainder of the extension shall be horizontal (4.9). | H M M L+ L | $150 $0 $50 $500 $800 |  |
|  |  | RECREATION BLD. (NEW) |  |  |  |
|  |  | Note: this structure was under construction at the time of inspection, thus no modifications are being recommended. |  |  |  |

The accessible parking at the Parks & Rec. Admin.		The sides of the curb ramp on the

School Building is sloped and partially blocks the		sidewalk to the Parks & Rec. Admin.

curb ramp.							building has excessive slopes.

The Parks & Rec. Admin. office has inadequate 			The men’s and women’s restrooms in the Parks & Rec.

signage and a door handle that requires pinching of		Admin. School Building have toilet flush controls and

the hand to operate.						toilet paper dispensers are not in correct locations.

The men’s and women’s restrooms in the Parks & Rec.		The entrance ramp to the Historic White House lacks

Admin. School Building have toilet flush controls and		adequate handrails and edge protection.

toilet paper dispensers are not in correct locations

The entrance to the Historic White House is narrow, has an excessive threshold and has a door handle that

requires pinching of the hand to operate.

The Senior Center accessible parking has an excessive		The curb ramp at the street level in front of the Senior

slope, lacks a “van accessible” space and access aisles.		Center has an excessive change in levels.

The east upper sidewalk at the Senior Center has		The men’s room in the Nutrition Center has

an excessive threshold.					inadequate maneuvering clearance on the pull side.

The men’s & women’s restrooms have narrow		The curb ramp in the Gymnasium parking has an

routes to accessible toilet stalls.				excessive change in levels.

The inner entrance to the gym has a panel type handle.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $18,500 |
| Medium’s | $22,350 |
| High’s | $12,500 |
| TOTAL | $53,350.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.