| Crystal Pond  Middletown Township (N.J.)  ADA Transition Plan Main Street (Port Monmouth) Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | No designated parking exists (dirt lot). | At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space (4.1.2(5)(b) & 4.6.4). | H | $2,500 |  |
| Picnic Areas | The picnic tables are not on accessible routes and lack adequate knee clearance depth. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level. At least one area should have a compliant table on an accessible route. Minimum knee clearances are: 27” high, 30” wide and 19” deep (4.3.2(2), 4.5.1 & 4.32.3). | M- | $1,800 |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $0 |
| Medium’s | $1,800 |
| High’s | $2,500 |
| TOTAL | $4,300.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.