| Dorsett Park  Middletown Township (N.J.)  ADA Transition Plan Devonshire Road Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | Two spaces are signed as accessible but no “van accessible” designation exists and spaces/access aisles are not striped. | At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Two spaces may share a common access aisle (4.1.2(5)(b) & 4.6). | H | $1,000 |  |
| Accessible Paths of Travel | The curb ramp at the accessible parking has a running slope up to 12%. The route to the ball field has a running slope up to 10% for approximately 20 feet near the bottom. | The maximum slope for ramps is 1:12 or 8.33% (4.8.2). The maximum slope for an accessible pedestrian route is 1:20 or 5% (4.3.7). | H L+ | $500 $3,000 |  |
| Play Ground | The play equipment surface is engineered wood chips. | Recommendation: this material has been generally accepted as “ADA compliant”, however, to maintain an adequate firm and level surface free of thresholds, this surface must be constantly maintained. We recommend using a rubber or corked surface. There are no ADA enforceable standards for playground areas, only guidelines at the present time; however, program access must still be met. | L+ | $3,000 |  |
| Ball Field | No designated wheelchair seating exists at the bleacher seating. | Recommendation: designate at least one location as wheelchair accessible seating. Ensure that the location provides an unobstructed line of sight. The designated wheelchair seating area should be large enough for at least 1 wheelchair user and 1 companion. A 60” by 60” minimum area would be preferred. Designation could be accomplished by painting the universal symbol of access on the pavement. | M | $1,000 |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $6,000 |
| Medium’s | $1,000 |
| High’s | $1,500 |
| TOTAL | $8,500.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.