| Fairview Soccer/Applebrook Pk.  Middletown Township (N.J.)  ADA Transition Plan Oak Hill Rd. Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | There are 7 designated accessible spaces that serve the soccer fields. None are designated as “van accessible” and all access aisles are 60” wide. There are 2 designated accessible spaces that serve the ball field. None are designated as “van accessible” and the access aisle is 60” wide. | At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Access aisles serving standard accessible spaces shall be at least 60” wide. Two spaces may share a common access aisle (4.1.2(5) & 4.6.4). At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Two spaces may share a common access aisle (4.1.2(5) & 4.6.4). | M+ M+ | $500 $500 |  |
| Accessible Paths of Travel | There is no accessible route to the bleacher area’s of the soccer and ball fields (rough & uneven grass). The concessions booth is not on an accessible route (rough & uneven grass). | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2(2) & 4.5.1). At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2(2) & 4.5.1). | H M | $8,000 $3,000 |  |
| Bleacher Seating | The soccer and ball fields have bleacher seating, however, neither have any designated wheelchair seating( | Recommendation: designate at least one location at each set of bleachers for each field. Reference the photo for placement to ensure other patrons do not block the line of sight for disabled patrons. Each designated wheelchair seating area should be large enough for 1 wheelchair user and 1 companion. A 60” by 60” minimum area would be preferred. Designation should be accomplished by painting the universal symbol of access on the pavement. | M+ | $750 |  |
| Concessions | The concessions counter is higher than 45”. | Transaction counters shall have a 36” maximum height, 36” minimum length. Equivalent facilitation might consist of a folding shelf attached to the main counter on which an individual with disabilities can write (4.5.2 & 7.2). | M- | $500 |  |

Bleacher seating has no designated wheelchair seating. We recommend

designating an area at each field as shown by the red rectangle.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $0 |
| Medium’s | $5,250 |
| High’s | $8,000 |
| TOTAL | $13,250.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.