| Gordon Court Park  Middletown Township (N.J.)  ADA Transition Plan Gordon Court (Port Monmouth) Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | No designated parking exists. | At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space (4.1.2(5)(b) & 4.6.4). | H | $500 |  |
| Accessible Paths of Travel | Two curb ramps at the parking level have lips of 3” ( The route to the ball field, playground and basketball court is rough and uneven grass. | Transitions from ramps to walks, gutters, or streets shall be flush and free of abrupt changes (4.7.2). At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | H M+ | $1,000 $7,500 |  |
| Play Ground | A threshold up to 6” encompasses the play equipment. The play equipment surface is engineered wood chips. | Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). Recommendation: this material has been generally accepted as “ADA compliant”, however, to maintain an adequate firm and level surface free of thresholds, this surface must be constantly maintained. We recommend using a rubber or corked surface. There are no ADA enforceable standards for playground areas, only guidelines at the present time; however, program access must still be met. | L+ L+ | $500 $3,000 |  |

Two curb ramps have excessive lips and the routes

to amenities such as play area, ball field, etc. is rough

and uneven grass.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $3,500 |
| Medium’s | $7,500 |
| High’s | $1,500 |
| TOTAL | $12,500.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.