| Hillside Park  Middletown Township (N.J.)  ADA Transition Plan Between Chestnut & Powell Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Pedestrian Paths of Travel | The routes to the tennis courts, basketball courts and ball field consist of rough and uneven grass. The southwest curb ramp has a 2” lip at the bottom and a running slope that exceeds 10%. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). Transitions from ramps to walks, gutters, or streets shall be flush and free of abrupt changes and slopes shall not exceed 1:12 or 8.33% (4.7.2 & 4.8.2). | M+ H | $8,500 $700 |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $0 |
| Medium’s | $8,500 |
| High’s | $700 |
| TOTAL | $9,200.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.