| Ideal Beach  Middletown Township (N.J.)  ADA Transition Plan Bayside Parkway Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Pedestrian Paths of Travel | The playground and beach are not on an accessible route (rough and uneven grass & sand). The route to the women’s restroom crosses a 2” change in levels( | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). | M+ M+ | $8,500 $300 |  |
| Parking | One space is signed as accessible and an additional space has striping but lacks signage. None are designated as “van accessible” and no access aisles exist. Note: accessible spaces exist in west lot only. Both lots have a total of 77 spaces. | Minimum 1 “van accessible” space and 3 standard accessible spaces. Access aisles serving van spaces shall be at least 96” wide and aisles serving standard accessible spaces shall be at least 60” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Two spaces may share a common access aisle (4.1.2(5)(b) & 4.6). Recommendation: install 1 “van accessible” space in each lot. The remaining 2 spaces should be located in the west lot. | H | $2,000 |  |
| Play Ground | The play equipment and surface lack accessible components. | Recommendation: as equipment is replaced, provide accessible components, transfer stations and surfacing. We recommend using the “ADA Accessibility Guidelines for Play Area’s”. | L | $8,000 |  |
| Public Restrooms | Men’s/Women’s: Signage is painted on doors( Sinks have 27” knee clearance to aprons and the push faucet control requires 8 lbs. force to operate. The women’s room mirror is 42” high to reflective surface. Accessible toilet stalls have the following barriers: 59” width, no rear grab bars, 37” high side grab bars, 15” high toilets, toilet paper dispensers on the open side wall and round door locks. | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign (4.30.4 & 4.30.6). Lavatories shall provide a clearance of at least 29” above the finish floor to the bottom of the apron. The force required to activate controls shall be no greater than 5 lbs. (4.19 & 4.27.4). Mirrors shall be mounted with the bottom edge of the reflecting surface no higher than 40” above the finish floor (4.19.6). The minimum width of the standard stall shall be 60”. A grab bar at least 36” long shall be located behind the water closet, with one end no farther than 6” from the inside corner of the stall. All grab bars shall be located 33” to 36” above the finish floor to the gripping surface. The height of water closets shall be 17” to 19”, measured to the top of the toilet seat. Toilet paper dispensers shall be below the side grab bar and at least 19” above the floor and no farther than 36” from the rear wall, measured to the far side of the dispenser. Handles, pulls, latches, locks, and other operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate (Figure 30, 4.16.3 & 4.13.9). | H L+ L M+ | $100 $300 $100 $1,500 |  |

The sidewalk to the women’s restroom has an abrupt				Restroom signage is not in

change in levels.								appropriate formats and locations.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $8,400 |
| Medium’s | $10,300 |
| High’s | $2,100 |
| TOTAL | $20,800.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.