| Kunkel / Leonardo Park  Middletown Township (N.J.)  ADA Transition Plan Brevent Avenue Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | The parking lot at the hockey rink has 3 designated accessible spaces but only 1 has signage. None are designated as “van accessible. The ground slopes up to 4%. The parking lot that serves the tennis courts has no designated accessible parking spaces. | Minimum 1 “van accessible” space and 1 standard accessible space. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Van spaces shall be served with an access aisle at least 96” wide. Two spaces may share a common access aisle. Parking spaces and access aisles shall be level with surface slopes not exceeding 1:50 or 2% in all directions (4.1.2(5) & 4.6). Minimum 1 “van accessible” space and 1 standard accessible space. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Van spaces shall be served with an access aisle at least 96” wide. Two spaces may share a common access aisle. Parking spaces and access aisles shall be level with surface slopes not exceeding 1:50 or 2% in all directions (4.1.2(5) & 4.6). | H H | $2,500 $500 |  |
| Pedestrian Paths of Travel | The route from the parking to the tennis court entrance crosses a curb. The curb ramp to the tennis court has a 1 ½” lip. The route to the ball field and tennis courts is rough and uneven grass. | Curb ramps shall be provided wherever an accessible route crosses a curb (4.7.1). Transitions from ramps to walks, gutters, or streets shall be flush and free of abrupt changes (4.7.2). At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2(2) & 4.5.1). | H M+ M+ | $750 $500 $6,500 |  |
| Hockey Rink | No designated wheelchair seating exists at the bleacher seating. Rink fences are eye level for wheelchair users. | Recommendation: designate at least one location on each side of the score keepers box. Each designated wheelchair seating area should be large enough for 1 wheelchair user and 1 companion. A 60” by 60” minimum area would be preferred. Designation should be accomplished by painting the universal symbol of access on the pavement. To ensure that these locations offer the patron a line of sight, they should be located directly behind the fence. Due to the fence height, we recommend either modifying the fence to a lowered height at each 60” by 60” location or raise the floor surface at each location to provide an unobstructed view. | M | $2,500 |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $0 |
| Medium’s | $9,500 |
| High’s | $3,750 |
| TOTAL | $13,250.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.