| Leonardo Beach  Middletown Township (N.J.)  ADA Transition Plan Beach Avenue Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Accessible Paths of Travel | The playground and beach are not on an accessible route (rough and uneven grass & sand). | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | M+ | $7,500 |  |
| Parking | No parking is designated (gravel lot). | At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Spaces shall be at least 96” wide. Two spaces may share a common access aisle. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Actual numbers of total accessible spaces needed should be determined by the total estimated number of spaces in this lot per table under 4.1.2 (4.1.2(5)(b) & 4.6.4). | H | $2,500 |  |
| Play Ground | A threshold up to 5” encompasses the play equipment. The play equipment surface is engineered wood chips. | Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). Recommendation: this material has been generally accepted as “ADA compliant”, however, to maintain an adequate firm and level surface free of thresholds, this surface must be constantly maintained. We recommend using a rubber or corked surface. There are no ADA enforceable standards for playground areas, only guidelines at the present time; however, program access must still be met. | L+ L+ | $500 $3,000 |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $3,500 |
| Medium’s | $7,500 |
| High’s | $2,500 |
| TOTAL | $13,500.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.