| Lincroft Acres Park  Middletown Township (N.J.)  ADA Transition Plan Orchard Hills Rd. (off Newman Springs Rd.) Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | No designated accessible spaces exist. Note: there are approx. 60 parking spaces in this lot. | Minimum 1 “van accessible” space and 2 standard accessible spaces. Access aisles serving van spaces shall be at least 96” wide and aisles serving standard accessible spaces shall be at least 60” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Two spaces may share a common access aisle (4.1.2(5)(b) & 4.6). | H | $1,500 |  |
| Pedestrian Paths of Travel | The route to the playground and soccer bleachers consists of rough and uneven grass/dirt. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | M+ | $2,500 |  |
| Soccer Fields | The soccer and ball fields have bleacher seating, however, neither have any designated wheelchair seating | Recommendation: designate at least one location at the bleachers. Reference the photo for placement to ensure other patrons do not block the line of sight for disabled patrons. Each designated wheelchair seating area should be large enough for 1 wheelchair user and 1 companion. A 60” by 60” minimum area would be preferred. Designation should be accomplished by painting the universal symbol of access on the pavement. | M | $500 |  |
| Play Ground | A threshold up to 6” encompasses the play equipment. The play equipment surface is engineered wood chips. | Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). Recommendation: this material has been generally accepted as “ADA compliant”, however, to maintain an adequate firm and level surface free of thresholds, this surface must be constantly maintained. We recommend using a rubber or corked surface. There are no ADA enforceable standards for playground areas, only guidelines at the present time; however, program access must still be met. | L+ L+ | $500 $3,000 |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $3,500 |
| Medium’s | $3,000 |
| High’s | $1,500 |
| TOTAL | $8,000.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.