| Lincroft Library  Middletown Township (N.J.)  ADA Transition Plan 722 Newman Springs Rd. Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | Designated accessible parking spaces lack a “van accessible” space. | At least 1 accessible space shall be designated as “van accessible” (4.6.4). | M | $50 |  |
|  |  | INTERIOR FEATURES |  |  |  |
| Miscellaneous Rooms and Spaces | Exit signs are not in accessible locations or formats. | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign (4.30.4 & 4.30.6). | H | $100 |  |
| Miscellaneous | The checkout counter exceeds 45” high. Numerous book shelves exceed maximum height for reach ranges. | Transaction counters shall have a 36” maximum height, 36” minimum length. Equivalent facilitation might consist of a folding shelf attached to the main counter on which an individual with disabilities can write (4.5.2 & 7.2). Recommendation: install signage directing patrons to contact library staff for assistance in obtaining materials if needed. | M H | $500 -- |  |
| Public Restrooms | Men’s/Women’s: Signage is located above doors and lacks an accessible format( Entrance doors have round knobs. Restrooms do not have visual/audible fire alarm devices. Sinks have 26 ½” knee clearance to aprons, exposed drain pipes and push water faucets that require 10 lbs. force to operate. The sink in the men’s room is in the clear floor space of the toilet stall door. Mirrors are 50” high to reflective surfaces. Accessible toilet stalls have the following deficiencies: round door locks, doors swing into clear floor space of stalls, 15” high toilets, inadequate grab bar lengths and placement and toilet paper dispensers that are 39” from rear walls. The urinal in the men’s room is 23” high to rim. The toilet flush control in the women’s accessible stall is located on the far side of toilet. | Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Where there is no wall space to the latch side of the door, signs shall be placed on the nearest adjacent wall. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door. Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille (4.30.4 & 4.30.6). Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs (4.13.9). At a minimum, visual signal appliances shall be provided in buildings and facilities in each of the following areas: restrooms and any other general usage areas (e.g., meeting rooms), hallways, lobbies, and any other area for common use (4.28.1). Lavatories shall provide a clearance of at least 29” above the finish floor to the bottom of the apron. Hot water and drain pipes exposed under sinks shall be insulated or otherwise configured so as to protect against contact. There shall be no sharp or abrasive surfaces under sinks. The force required to activate controls shall be no greater than 5 lbs. (4.19 & 4.27.4). Recommendation: relocate sink. Mirrors shall be mounted with the bottom edge of the reflecting surface no higher than 40” above the finish floor (4.19.6). Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs. The height of water closets shall be 17” to 19”, measured to the top of the toilet seat. The rear grab bar shall be at least 36” long and the side bar shall be at least 42” long. All grab bars shall be located 33” to 36” above the finish floor to the top gripping surface. Placement of grab bars shall comply with Figure 30. Toilet paper dispensers shall be below the grab bar and at least 19” above the floor and no farther than 36” from the rear wall, measured to the far side of the dispensers (4.13.9 & Figure 30). Recommendation: re-hinge doors to swing out of stalls. Urinals shall be stall-type or wall-hung with an elongated rim at a maximum of 17” above the finish floor. Flush controls shall be mounted no more than 44” above the finish floor (4.18.2 & 4.18.4). Flush controls shall be mounted on the wide side of toilet areas (4.16.5). | M+ M+ H M- M+ L+ M L L+ | $100 $100 $900 $500 -- $100 $750 $1,000 $300 |  |

Restroom signage is located in an inaccessible locations and formats. Door

hardware requires grasping, pinching and turning of the wrist to operate.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $1,400 |
| Medium’s | $2,000 |
| High’s | $1,000 |
| TOTAL | $4,400.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.