| MTT Park  Middletown Township (N.J.)  ADA Transition Plan Newman Springs Rd. Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | The parking lot serving ball fields 7 & 8 has more than 70 total spaces, none of which are designated as accessible. The parking lot serving ball fields 5 & 6 is gravel and no designated parking exists. | Minimum 1 “van accessible” space and 2 standard accessible space. Access aisles serving van spaces shall be at least 96” wide and aisles serving standard accessible spaces shall be at least 60” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Two spaces may share a common access aisle (4.1.2(5)(b) & 4.6). At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Spaces shall be at least 96” wide. Two spaces may share a common access aisle. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Actual numbers of total accessible spaces needed should be determined by the total estimated number of spaces in this lot per table under 4.1.2 (4.1.2(5)(b) & 4.6.4). | H H | $1,000 $750 |  |
| Accessible Paths of Travel | The pedestrian path of travel to the playground and ball fields consists of rough and uneven grass. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | M+ | $8,500 |  |
| Play Ground | A threshold up to 5” encompasses the play equipment. The play equipment surface is engineered wood chips. | Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). Recommendation: this material has been generally accepted as “ADA compliant”, however, to maintain an adequate firm and level surface free of thresholds, this surface must be constantly maintained. We recommend using a rubber or corked surface. There are no ADA enforceable standards for playground areas, only guidelines at the present time; however, program access must still be met. | L+ L+ | $500 $3,000 |  |
| Ball Fields | Bleacher seating has no designated wheelchair accessible locations. | Recommendation: designate at least one location as wheelchair accessible seating at each field. Ensure that the location provides an unobstructed line of sight. The designated wheelchair seating area should be large enough for at least 1 wheelchair user and 1 companion. A 60” by 60” minimum area would be preferred. Designation could be accomplished by painting the universal symbol of access on the pavement. Additionally, ball fields 2, 3 and 4 are not accessible due to numerous significant barriers, including restrooms. We recommend focusing on making the other fields as accessible and usable as possible and providing a base line accessible restroom to serve the complex. | M | $5,500 |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $3,500 |
| Medium’s | $14,000 |
| High’s | $1,750 |
| TOTAL | $19,250.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.