| Middletown Swim Club  Middletown Township (N.J.)  ADA Transition Plan Harmony Road Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | Five spaces are signed as accessible, none of which are designated as “van accessible”. The ground has a slope up to 5%. Note: approximately 232 parking spaces exist. | Minimum 1 “van accessible” space and 6 standard accessible spaces. Access aisles serving van spaces shall be at least 96” wide and aisles serving standard accessible spaces shall be at least 60” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Two spaces may share a common access aisle. Parking spaces and access aisles shall be level with surface slopes not exceeding 1:50 (2%) in all directions (4.1.2(5)(b) & 4.6). | H | $2,000* |  |
| Pedestrian Paths of Travel | The walkway between #3 & #4 has a running slope up to 7%( The walkway between #1 & #6 has a running slope up to 19%( The route to the snack bar crosses multiple steps( | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | M+ | $5,500* |  |
| Swimming Pools | The Pool “C” ramp has only 1 handrail 42” high with inadequate extensions. None of the pools offer access to the water. | If a ramp run has a rise greater than 6” or a horizontal projection greater than 72”, then it shall have handrails on both sides. If handrails are not continuous, they shall extend at least 12” beyond the top and bottom of the ramp segment and shall be parallel with the floor or ground surface. Top of handrail gripping surfaces shall be mounted between 34” and 38” above ramp surfaces (4.3.7 & 4.8.5). Recommendation: install an independently operated device such as a lift pump to serve at least one pool. | M+ M | $1,500 $5,000 |  |
| Cabana’s | Small and large cabanas exist with varying amenities, none of which are accessible from the exterior (steps and grass). | Recommendations: modify at least 1 type of each cabana to be accessible. Each accessible unit should be on an accessible route and should have accessible amenities inside. | M+ | $15,000* |  |
| Public showers / Restrooms | Men’s/Women’s #3: Signs are mounted on doors. Mirrors are 60” high to reflective surfaces. Accessible toilet stalls have inadequately placed grab bars and lack rear bars. Toilet paper dispensers are located 46” from rear wall( Showers have multiple barriers such as: 10” curbs, inadequate grab bars, high shower heads, etc. Note: five other showers / restrooms lack adequate clear floor space to accommodate accessible fixtures. | Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign (4.30.6). Mirrors shall be mounted with the bottom edge of the reflecting surface no higher than 40” above the finish floor (4.19.6). The rear grab bar shall be at least 36” long and the side bar shall be at least 42” long. All grab bars shall be located 33” to 36” above the finish floor to the top gripping surface. Placement of grab bars shall comply with Figure 30. Toilet paper dispensers shall be below the grab bar and at least 19” above the floor and no farther than 36” from the rear wall, measured to the far side of the dispensers (4.16.5). Recommendations: either a 36” x 36” or 30” wide by 60” long shower should be installed. Grab bars should comply with Figure 37. If provided, curbs in shower stalls 36” by 36” shall be no higher than ½”. Shower stalls that are 30” by 60” minimum shall not have curbs. A shower spray unit with a hose at least 60” long that can be used both as a fixed shower head and as a hand-held shower shall be provided. EXCEPTION: In unmonitored facilities where vandalism is a consideration, a fixed shower head mounted at 48” above the shower floor may be used in lieu of a hand-held shower head (4.21). Recommendations: modify restroom #3 to be fully accessible and post signage at inaccessible restrooms that give the location of restroom #3. | M+ L+ M+ L+ | $100 $200 $300 $7,000 |  |
| Storage Barn | This structure is only accessible to town staff. | No recommendations are currently being made due to lack of public access. |  |  |  |
|  |  | GENERAL RECOMMENDATIONS |  |  |  |
|  |  | Ensure that at least 1 accessible route connects each park amenity together, from parking to entrances to pools to cabana’s, etc. |  |  |  |

The walkways between #3 & #4 and between #1 & #6 have excessive slopes.

The only route to the snack bar is via steps.				The ramp to Pool “C” has only 1 handrail and it is too

high.

Toilet stalls in Building 3 have inadequate grab bars,

misplaced  toilet paper dispensers, etc.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $7,200 |
| Medium’s | $27,400 |
| High’s | $2,000 |
| TOTAL | $36,600.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.