| New Monmouth Library  Middletown Township (N.J.)  ADA Transition Plan 55 New Monmouth Rd. Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | West parking lot: Access aisle serving van accessible space is 92” wide. East parking lot: This lot is a staff only lot and the entrance door is only accessible by staff. | Access aisles serving “van accessible” parking spaces shall be at least 96” wide (4.1.2(5)(b)). No recommendations are currently being made due to restricted public access. | M -- | $50 -- |  |
|  |  | INTERIOR FEATURES |  |  |  |
| Miscellaneous Rooms and Spaces | Exit signs are not in accessible locations or formats and do not indicate which exits are accessible. The Community Wing and Children’s Room’s have signage mounted in inaccessible locations and formats( Meeting and other rooms/offices have signage mounted at heights ranging between 48” and 52” to the center. | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign (4.30.4 & 4.30.6). Recommendation: install egress signage that indicates whether or not an exit is accessible. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Where there is no wall space to the latch side of the door, signs shall be placed on the nearest adjacent wall. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door. Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille (4.30.4 & 4.30.6). Mounting height shall be 60’ above the finish floor to the centerline of the sign on the wall adjacent to the latch side of the door (4.30.6). | H H H | $300 $100 -- |  |
| Miscellaneous | The checkout counter exceeds 45” high. Numerous book shelves exceed maximum height for reach ranges. Study carrels and tables have inadequate knee clearances. | Transaction counters shall have a 36” maximum height, 36” minimum length. Equivalent facilitation might consist of a folding shelf attached to the main counter on which an individual with disabilities can write (7.2). Recommendation: install signage directing patrons to contact library staff for assistance in obtaining materials if needed. At least 5 percent or a minimum of one of each element of fixed seating, tables, or study carrels shall comply with 4.32. Minimum knee clearances are: 27” high, 30” wide and 19” deep (8.2 & 4.32.3). | M H M+ | $500 $50 $1,000 |  |
| Public Restrooms | Community Wing Restrooms: Entrance doors require more than 10 lbs. force to open. Lavatories have 28” knee clearance to aprons. Mirrors are 41” high to reflective surfaces. Side grab bars in accessible toilet stalls extend 48” from rear walls. Unisex Restroom: Signage is mounted 48” high to center. Entrance door requires more than 10 lbs. force to open. The side grab bar extends 48” from the rear wall. | 5 lbs. maximum for interior hinged doors with closers (4.13.11). Lavatories shall provide a clearance of at least 29” above the finish floor to the bottom of the apron (4.19.2). Mirrors shall be mounted with the bottom edge of the reflecting surface no higher than 40” above the finish floor (4.19.6). A grab bar shall be mounted adjacent to the water closet on the side wall and extend from no more than 12” from the back wall to at least 52” from the back wall (Figure 30(a)). Mounting height shall be 60’ above the finish floor to the centerline of the sign on the wall adjacent to the latch side of the door (4.30.6). 5 lbs. maximum for interior hinged doors with closers (4.13.11). A grab bar shall be mounted adjacent to the water closet on the side wall and extend from no more than 12” from the back wall to at least 52” from the back wall (Figure 30(a)). | M+ L L- L+ H M+ L+ | $0 $500 $200 $100 $0 $0 $100 |  |

The Community Wing and Children’s room signage

are in inaccessible locations and formats.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $900 |
| Medium’s | $1,550 |
| High’s | $450 |
| TOTAL | $2,900.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.