| Poricy Park  Middletown Township (N.J.)  ADA Transition Plan Oak Hill Road Spring 2008 |
| --- |
| S |  |  |  |  |  |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| MISC. EXTERIOR FEATURES |
| Miscellaneous Parking | The lot that serves the Nature Center has 4 spaces signed as accessible but none have access aisles and no “van accessible” designation exists( | At least one accessible space shall be designated as “van accessible”. Access aisles serving van spaces shall be at least 96” wide and aisles serving standard accessible spaces shall be at least 60” wide. Two spaces may share a common access aisle (4.1.2(5)(b) & 4.6). | H | $1,000 |  |
| Pedestrian Paths of Travel | The route from this parking lot to the Nature Center entrance crosses two changes in level greater than 1”( The route to picnic areas consists of rough and uneven grass. | Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). Recommendations: install at least 5% of accessible picnic tables and grills, but not less than one should be on an accessible route. | H M+ | $500 $1,000 |  |
|  |  | NATURE CENTER BLDG. |  |  |  |
| Entrance | The door hardware requires pinching of the hand to operate( The entrance has a 2” threshold( The inner entrance doors require 7 lbs. force to open. | Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs (4.13.9). Thresholds at doorways shall not exceed ½” beveled (4.13.8). 5 lbs. maximum for interior hinged door (4.13.11). | H H M+ | $50 $200 $0 |  |
| Miscellaneous Rooms and Spaces | Exit signs are not in accessible locations or formats The classroom entrance is 30” wide. | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign (4.30.4 & 4.30.6). Doorways shall have a minimum clear opening of 32” with the door open 90 degrees, measured between the face of the door and the opposite stop (4.13.5). | H M | $100 $1,000 |  |
| Public Restrooms | Men’s/Women’s: Signage is not in accessible format and location( Entrance doors require 10 lbs. force to open. Sinks have 27 ½” knee clearance at apron and exposed drain pipes. Mirrors are 47” high to reflective surface. Alarm notification devices are mounted on ceilings. Accessible toilet stalls are narrow (alternate stalls). The urinal in the men’s room is 24” high to rim. | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign (4.30.4 & 4.30.6). 5 lbs. maximum for interior hinged doors (4.13.11). Lavatories shall provide a clearance of at least 29” above the finish floor to the bottom of the apron. Hot water and drain pipes exposed under sinks shall be insulated or otherwise configured so as to protect against contact (4.19). Mirrors shall be mounted with the bottom edge of the reflecting surface no higher than 40” above the finish floor (4.19.6). Alarms shall be placed 80” above the highest floor level within the space or 6” below the ceiling, whichever is lower (4.28.3). Recommendation: if structurally practical, a “standard” stall per 4.17 should be installed in each restroom. If however, this is not practical, we recommend installing an accessible “unisex” restroom in an alternate location. Signage should be installed at inaccessible restrooms giving the location of the nearest accessible restroom. Urinals shall be stall-type or wall-hung with an elongated rim at a maximum of 17” above the finish floor. Flush controls shall be mounted no more than 44” above the finish floor (4.18.2 & 4.18.4). | H M M+ L H M L | $100 $0 $400 $200 $400 $8,000* $1,500 |  |
|  |  | ANNEX CENTER BLDG. |  |  |  |
| Parking | No designated accessible spaces exist. | At least 1 accessible space shall be designated as “van accessible” and served by an access aisle at least 96” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space (4.1.2(5)(b) & 4.6.4) | H | $1,000 |  |
| Entrance | Door opening hardware consists of a round knob. A 6 ½” step exists at the entrance door( | Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs (4.13.9). Thresholds at doorways shall not exceed ½” beveled (4.13.8). | H H | $50 $1,000 |  |
|  |  | FARM HOUSE & BARN |  |  |  |
| Pedestrian Paths of Travel | The route to both structures crosses rough and uneven grass. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | H | $2,500 |  |
| Entrance | The entrance to the Farm House crosses 4 feet of stairs. | Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). Recommendations: these are historic structures. The Farm House offers classes and shows throughout the year. If adding a ramp or lift will destroy the historic integrity of the structure, we recommend relocation those programs to an accessible location. | H | $5,000* |  |

The parking lot near the Nature Center lacks access		This change in levels exists on the route from the

aisles and a “van accessible” parking space.			parking lot to the Nature Center entrance.

This change in levels exists on the route from the		The Nature Center entrance has door handles that

parking lot to the Nature Center entrance.			require grasping and pinching to operate.

The entrance to the Nature Center has an excessive		The restrooms in the Nature Center have inaccessible

threshold.							formats and are not in correct locations.

The Annex Center entrance has a step and a door

handle that requires grasping and pinching to operate.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $1,700 |
| Medium’s | $3,200 |
| High’s | $11,900 |
| TOTAL | $16,800.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.