| Port Monmouth Train Station  Middletown Township (N.J.)  ADA Transition Plan Carter Avenue Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Middletown Helps it’s Own Bldg. | The parking lot is loose gravel. The route from the parking area to the sidewalk has a 2” threshold. | Minimum 1 “van accessible” space. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Van spaces shall be served with an access aisle at least 96” wide. Parking spaces and access aisles shall be level with surface slopes not exceeding 1:50 or 2% in all directions (4.1.2(5) & 4.6). Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). | H H | $2,500 $300 |  |
| Caboose | The caboose is not a functioning structure currently. | Note: no recommendations are currently being made based on usage. | -- | -- |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $0 |
| Medium’s | $0 |
| High’s | $2,800 |
| TOTAL | $2,800.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.