| Public Works Complex  Middletown Township (N.J.)  ADA Transition Plan 52 Kanes Ln. Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
|  |  | NOTE: the main garage, storage barns 1 & 2 and the recycling storage shed do not provide services or programs to the public. Due to usage, these structures were not inspected. |  |  |  |
| Parking | Two accessible parking spaces exist but none are designated “van accessible”. Only one of the spaces are served with an access aisle( | At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Access aisles serving standard accessible spaces shall be at least 60” wide. Two spaces may share a common access aisle (4.1.2(5) & 4.6.4). | H | $500 |  |
| Accessible Paths of Travel | The curb ramp at the accessible parking has a running slope up to 17%( The cross slope on the route to the entrance slopes up to 7%( | 1:12 or 8.33% maximum slope (4.8.2). Nowhere shall the cross slope of an accessible route exceed 1:50 or 2% (4.3.7). | H M+ | $2,500 $3,500 |  |
|  |  | INTERIOR FEATURES |  |  |  |
| Miscellaneous Rooms and Spaces | The exit sign is not in an accessible location or format. | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign (4.30.4 & 4.30.6). | H | $50 |  |
| Transaction Counter | The counter is 39” high and 30” long( | Counters maximum height shall be 36” and minimum length shall be 36” (7.2). | M | $750 |  |

One of the accessible parking spaces lack an access		The curb ramp serving the accessible parking spaces

aisle.								has an excessive running slope.

The exterior route to the 				The interior transaction counter is too high and not long

entrance has an excessive cross				enough.

slope.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $0 |
| Medium’s | $4,250 |
| High’s | $3,050 |
| TOTAL | $7,300.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors.