| Shorecrest Park  Middletown Township (N.J.)  ADA Transition Plan Pine St. & Stephenville Blvd. Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Pedestrian Paths of Travel | The entrance route from street level has a running slope up to 12%( The route to the playground consists of rough and uneven grass/dirt. | An accessible route that exceeds 1:20 or 5%, is to be considered a ramp. Ramps that have a vertical rise of more than 6” or a horizontal projection more than 72”, shall have handrails on both sides (4.3.7 & 4.8.5). At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | H M- | $1,500 $2,500 |  |
| Play Ground | A threshold up to 6” encompasses the play equipment. The play equipment surface is engineered wood chips. | Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). Recommendation: this material has been generally accepted as “ADA compliant”, however, to maintain an adequate firm and level surface free of thresholds, this surface must be constantly maintained. We recommend using a rubber or corked surface. There are no ADA enforceable standards for playground areas, only guidelines at the present time; however, program access must still be met. | L+ L+ | $500 $3,000 |  |

The street level entrance has an excessive slope.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $3,500 |
| Medium’s | $2,500 |
| High’s | $1,500 |
| TOTAL | $7,500.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.