| Tindall Park  Middletown Township (N.J.)  ADA Transition Plan Tindall Road Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Misc. Accessible Paths of Travel | The path of travel from accessible parking to the tennis courts crosses rough, uneven grass( The path of travel to the east tennis courts crosses a 1 ½” threshold( The entrance to the west tennis courts is sloped up to 14%( The path of travel to the basketball courts consists of rough, uneven grass with excessive slopes ( The route to the play equipment is rough and uneven( | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2(2) & 4.5.1). Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). The maximum slope on an accessible path of travel is 1:20 or 5% (4.3.7). At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level. The maximum slope on an accessible path of travel is 1:20 or 5% (4.3.2(2), 4.3.7 & 4.5.1). At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level. The maximum slope on an accessible path of travel is 1:20 or 5% (4.3.2(2), 4.3.7 & 4.5.1). | M M H M L+ | $2,500 $200 $500 $5,000 $1,500 |  |
| Misc. Parking | Accessible spaces near the tennis courts lack a “van accessible” space and access aisles are 60” wide. The basketball courts have approximately 6 parking spaces provided, none of which are designated as being accessible. | At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Two spaces may share a common access aisle (4.1.2(5)(b) & 4.6.4). At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space (4.1.2(5)(b) & 4.6.4). | M M+ | $500 $500 |  |
| Picnic Areas | Picnic Tables and barbecue grills are not on accessible paths of travel (rough, uneven grass). Picnic tables lack adequate knee clearance depth. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level. Knee clearance at accessible tables shall have at least 19” depth (4.3.2 & 4.32.3). Recommendations: install at least 5% of accessible picnic tables and grills, but not less than one should be on an accessible route. | L+ | $2,500 |  |
| Play Area | Play equipment and surface lack accessible components/features. | Recommendation: if feasible based on usage, install accessible equipment and surface as described in the “Best Practice Guidance for Play Areas”. | L | $8,000 |  |
| Miscellaneous Structures | The Pigeon Club structure is not accessible and is not on an accessible route. NOTE: staff indicated during our on site visit that this structure is not currently used for any public access and serves as storage for parks equipment only. | Recommendation: due to structure usage, we are not recommending any modifications for accessibility. If in the even that future usage changes, barriers such as accessible routes and entrance access will need to be addressed. | -- | -- |  |
| Miniature Golf Course | Three parking spaces are signed and striped as accessible, however, no “van accessible” designation exists and access aisles are 60” wide. The concessions counter has a 3” step up in front of it and the counter is more than 50” high( | At least 1 accessible space shall be designated as “van accessible” and be served with an access aisle at least 96” wide. Access aisles serving standard accessible spaces shall be at least 60” wide. Two spaces may share a common access aisle (4.1.2(5) & 4.6.4). Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp. Transaction counters shall have a 36” maximum height, 36” minimum length. Equivalent facilitation might consist of a folding shelf attached to the main counter on which an individual with disabilities can write (4.5.2 & 7.2). | H M | $400 $900 |  |

Access aisles serving accessible parking at the tennis		The route to the east tennis court crosses a 1 ½”

courts are too narrow. There is no firm and stable		threshold.

route to the tennis courts.

The entrance at the west tennis courts has an 			There are no designated accessible parking spaces at

excessive slope.							the basketball courts and the route to the courts is

rough and uneven with excessive slopes.

The route to access the playground equipment is rough		The route to access the miniature golf course consists

and uneven.							of rough and unstable loose rock.

The route to access the miniature golf course consists		A 3” threshold exists in front of the concessions booth.

of rough and unstable loose rock.

The concessions counter significantly exceeds the

maximum height allowance.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $900 |
| Medium’s | $9,600 |
| High’s | $9,500 |
| TOTAL | $20,000.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors.