| Township Municipal Complex  Middletown Township (N.J.)  ADA Transition Plan 1 Kings Highway/Route 35 Spring 2008 |
| --- |
| S |  |  |  |  |  |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| TOWN HALL ADMIN. BLD. |
| Parking | Two spaces are signed as accessible but none are designated “van accessible”. Access aisle is 60” wide( | At least one accessible space shall be designated as “van accessible”. Access aisles serving van spaces shall be at least 96” wide (4.1.2(5)(b) & 4.6). | H | $500 |  |
| Pedestrian Paths of Travel | The curb ramp at street level has a running slope up to 12%( NOTE: the curb ramp was blocked by a parked car at the time of inspection. The diameter of the upper ramp handrails exceed 1 ½”( | 1:12 or 8.33% maximum slope (4.8.2). Recommendation: paint the curb ramp a contrasting color and install “no parking” signage. The diameter or width of the gripping surfaces of a handrail or grab bar shall be 1 ¼” to 1 ½” (4.26.2). | H M | $800 $2,000 |  |
| Interior Features | Interior signs lack accessible formats and locations (exits, offices, conference room, etc.). Interior doors have panel hardware and require more than 10 lbs. force to open( The drinking fountain by the Mayors Office has 29” knee clearance( The stairs to the basement lack adequate hand rail extensions( The ramp between the Mayors Office and the Municipal Court has a running slope up to 12% and handrails are 32” high( | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door (4.30.4 & 4.30.6). Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs. Interior hinged doors shall not exceed 5 lbs. force to open (4.13). Objects projecting from walls with their leading edges between 27” and 80” above the finished floor shall protrude no more than 4” into walks, halls, corridors, passageways, or aisles (4.4.1). Recommendation: modify the knee clearance of the fountain to 27”. If handrails are not continuous, they shall extend at least 12” beyond the top riser and at least 12” plus the width of one tread beyond the bottom riser. At the top, the extension shall be parallel with the floor or ground surface. At the bottom, the handrail shall continue to slope for a distance of the width of one tread from the bottom riser; the remainder of the extension shall be horizontal (4.9.4). 1:12 or 8.33% maximum slope. Top of handrail gripping surfaces shall be mounted between 34” and 38” above ramp surfaces (4.8). | H M+ M+ L M+ | $300 $150 $200 $750 $1,500 |  |
|  |  | POLICE DEPT./MUNICIPAL COURT |  |  |  |
| Exterior Pedestrian Paths of Travel | Entrance ramp handrails do not have adequate extensions at the top and bottom of the ramp( | If handrails are not continuous, they shall extend at least 12” beyond the top and bottom of the ramp segment and shall be parallel with the floor or ground surface (4.8.5). | M+ | $1,500 |  |
| Entrance | The inner entrance power assist doors require 19 lbs. force to open. | 5 lbs. maximum force for interior hinged doors (4.13.11). | H | $0 |  |
| Interior Rooms and Spaces | Interior signs lack accessible formats and locations (exits, offices, court room, stairway, etc.)( | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door (4.30.4 & 4.30.6). | H | $400 |  |
| Lobby Restrooms | Entrance doors require 9 lbs. force to open. Toilet paper dispensers in accessible stalls are 40” from rear walls. Grab bars in accessible toilet stalls are 37” high to top. | 5 lbs. maximum for interior hinged doors (4.13.11). Toilet paper dispensers shall be below the grab bar and no farther than 36” from the rear wall, measured to the far side of the dispensers (Figure 30). All grab bars shall be located 33” to 36” above the finish floor to the gripping surface (Figure 30). | M L+ L | $0 $100 $200 |  |
| Pay Telephone | The coin slot is 57” high. | 54” maximum side reach (4.2.6). | L | $200 |  |
| Municipal Court | The ticket counter is 43” high( There are no designated wheelchair seating locations in the court room/commission chambers (pew seating)( No Assistive Listening System exists in the court room/commission chamber. | Counters maximum height shall be 36” and minimum length shall be 36” (7.2). Minimum 4 wheelchair seating locations (4.1.3(19)). Recommendation: install wheelchair locations near the front of the room. In assembly areas where audible communications are integral to the use of the space (e.g., concert and lecture halls, playhouses and movie theaters, meeting rooms, etc.) shall have a permanently installed assistive listening system if (1) they accommodate at least 50 persons, or if they have audio-amplification systems, and (2) they have fixed seating. The minimum number of receivers to be provided shall be equal to 4 percent of the total number of seats, but in no case less than two. Signage shall be installed to notify patrons of the availability of a listening system (4.1.3(19(b)). | H M+ M+ | $500 $500 $1,600 |  |
|  |  | JOHNSON-GILL ANNEX |  |  |  |
| Parking | Two spaces are signed as accessible but none are designated as “van accessible”. The far east space is sloped up to 3%( Note: more than 120 spaces exist in this lot. | Minimum 1 “van accessible” space and 4 standard accessible spaces. Access aisles serving van spaces shall be at least 96” wide and aisles serving standard accessible spaces shall be at least 60” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Two spaces may share a common access aisle. Parking spaces and access aisles shall be level with surface slopes not exceeding 1:50 (2%) in all directions (4.1.2(5)(b) & 4.6). | H | $2,500 |  |
| Exterior Pedestrian Paths of Travel | The route to the entrance crosses a 1” change in levels( | Changes in level up to ¼” may be vertical and without edge treatment. Changes in level between ¼” and ½” shall be beveled with a slope no greater than 1:2. Changes in level greater than ½” shall be accomplished by means of a ramp (4.5.2). | H | $500 |  |
| Entrance | The main entrance door has panel type handles and a ¾” threshold( | Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs. Thresholds at doorways shall not exceed ½” beveled (4.13). | H | $200 |  |
| Interior Rooms and Spaces | Interior signs lack accessible formats and locations (exits, offices, restrooms, etc.)( Office entrance doors require 10 lbs. force to open and have panel type handles. | Letters and numerals shall be raised 1/32”, upper case, sans serif or simple serif type and shall be accompanied with Grade 2 Braille. Where permanent identification is provided for rooms and spaces, signs shall be installed on the wall adjacent to the latch side of the door. Mounting height shall be 60’ above the finish floor to the centerline of the sign. Mounting location for such signage shall be so that a person may approach within 3” of signage without encountering protruding objects or standing within the swing of a door (4.30.4 & 4.30.6). Operating devices on accessible doors shall have a shape that is easy to grasp with one hand and does not require tight grasping, tight pinching, or twisting of the wrist to operate. Lever-operated mechanisms, push-type mechanisms, and U-shaped handles are acceptable designs. Interior hinged doors shall not exceed 5 lbs. force to open (4.13). | H H | $400 $100 |  |
| Tax Collections Office | The transaction counter is 32” long. The accessible computer station is 29” high and sticks out more than 8” from the wall( | Transaction counter shall be at least 36” long (7.2). Objects projecting from walls with their leading edges between 27” and 80” above the finished floor shall protrude no more than 4” into walks, halls, corridors, passageways, or aisles (4.4.1). Recommendation: modify the knee clearance of the table to 27” high. | L+ M+ | $350 $100 |  |
| Drinking Fountain | One lowered fountain exists for wheelchair users. | Where only one drinking fountain is provided on a floor there shall be a drinking fountain which is accessible to individuals who use wheelchairs and one accessible to those who have difficulty bending or stooping (4.1.3(10)(a)). | L | $400 |  |
| Public Restrooms | Entrance doors require 10 lbs. force to open. Sink drain pipes are exposed. Mirrors are 50” high to reflective surfaces. The flush control in the men’s accessible toilet stall is located on the far side of toilet( | Interior hinged doors shall not exceed 5 lbs. force to open (4.13.11). Hot water and drain pipes exposed under sinks shall be insulated or otherwise configured so as to protect against contact (4.24.6). Mirrors shall be mounted with the bottom edge of the reflecting surface no higher than 40” above the finish floor (4.19.6). Flush controls shall be mounted on the wide side of toilet areas (4.16.5). | M+ M+ L L+ | $0 $100 $100 $300 |  |
|  |  | COMMUNITY CENTER |  |  |  |
|  |  | Recommendation: this structure has little or no public access. We are not recommending any immediate barrier removal actions. If in the event that the future usage changes, identified barriers should be incorporated for basic access as well as maintaining the historical integrity of the structure | -- | -- |  |

Accessible parking serving the Admin. Bldg. 		The curb ramp on the accessible route to the

lacks “van accessible” designation and 96” min.		Administrative offices is too steep.

width access aisle.

The upper entrance ramp hand				Interior doors in the Admin. office

rails have a diameter larger than				have inaccessible door handles.

the maximum allowed (Admin.).

The drinking fountain by the Mayors office protrudes			Stairway handrails in the Admin.

into the hallway.							offices lack adequate extensions.

The ramp between the Mayors				The entrance ramp to the Police department has

Office and Court room is too steep.			inadequate handrail extensions at the top and bottom.

Interior offices on the Police Dept. side of Town Hall lack signage with accessible formats and accessible locations.

The Municipal Court ticket				The Municipal Court/Commission meeting room

counter is too high.					lacks wheelchair seating locations.

Parking for the Annex Bld. lacks “van accessible”		The route to the Annex bld. crosses a 1” change

signage and slopes on the east end.				in levels.

The entrance to the Annex Building has panel door handles and an excessive threshold.

Offices and rooms in the Annex Building have		The accessible computer in the Annex Bldg. Tax

signage in inaccessible locations and formats.		Collections office, protrudes too far from the wall.

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $2,400 |
| Medium’s | $7,650 |
| High’s | $6,200 |
| TOTAL | $16,250.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.

# Text boxes

Sloped