| West Front St. Park  Middletown Township (N.J.)  ADA Transition Plan West Front Street Spring 2008 |
| --- |
| Location | Identified Barrier(s) | Recommended Corrective Action Based on ADAAG or Applicable Guideline | Priority: L=Low M=Medium H=High | *Cost Estimate | Barrier Removal Target Date & Notes |
| EXTERIOR FEATURES |
| Parking | One space is signed as accessible but no “van accessible” designation exists and spaces/access aisles are hard to measure due to significant fading. Note: at least 40 total spaces exist. | Minimum 1 “van accessible” space and 1 standard accessible space. Aisles serving van spaces shall be at least 96” wide. Signs shall be located so they cannot be obscured by a vehicle parked in the space. Two spaces may share a common access aisle (4.1.2(5)(b) & 4.6). | H | $1,000 |  |
| Accessible Paths of Travel | The route to the soccer fields is rough and uneven grass. | At least one accessible route shall connect accessible buildings, facilities, elements, and spaces that are on the same site. Ground and floor surfaces along accessible routes shall be stable, firm, slip-resistant and free of abrupt changes in level (4.3.2). | M+ | $4,000 |  |

| Priority Level | Cost Estimate Totals |
| --- | --- |
| Low’s | $0 |
| Medium’s | $4,000 |
| High’s | $1,000 |
| TOTAL | $5,000.00* |

* Cost estimates are given as general guidance only.  Actual construction costs will vary depending on availability of materials and contractors used and the type of barrier removal utilized.